## Slide 1: Parameter dependency check of couple mode theory in time

## Slide 2: Couple mode theory in time
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect.式(2) )
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect.式(3) )

## Slide 3: 參數
(wavelength =1.55945 um)
(wavelength = 1.558 um)
c : speed of light in vacuum (299792458e6 um/s)
cavity length (31.41592 um, 5um radius ring)
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect. TABLE. 1)
: effective cross section of Kerr effect (0.204 um^2)
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect. TABLE. 1)
：index change per Kelvin (0.000195 1/K)
(refer: Thermal Modelling of Silicon Photonic Ring Modulator with Substrate Undercut 式(1)內參數)

## Slide 4
：amplitude couple photon life time (7.75369666558376 ps)
amplitude photon life time : 7.650191072370922 ps
：linear absorption coefficient (34.74051370464404 1/cm)
Two photon absorption coefficient (5e-13 cm/mW)
(refer: Measurement of the Nonlinear Loss and Effective Free Carrier Lifetime in Silicon Microring Resonators 式(10))
effective cross section of Two-photon absorption effect (0.1289 um^2)
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect. TABLE. 1)
effective FCA cross section (1.04e-17 cm^2)
(refer: Measurement of the Nonlinear Loss and Effective Free Carrier Lifetime in Silicon Microring Resonators 式(10))
N：Free carrier density (1/cm^3)
：Input Laser field amplitude

## Slide 5
Thermal time constant (fitting value =17.5ns )
：density of Silicon (2.329e-12 g/um^3)
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect. TABLE. 1)
： specific heat capacity of silicon (713.0 mJ/(g*K))
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect. TABLE. 1)
：Photon round trip time (0.4174730024555257 ps)
：Free carrier life time (fitting value = 0.5 ns)
：photon energy (0.0001274983842559692 fJ)
： effective cross section of Free carrier absorption (0.116 um^2)
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect. TABLE. 1)
： effective cross section of Free carrier absorption (0.116 um^2)
(refer: Multi bistability and self-pulsation in nonlinear high- Q silicon microring resonators considering thermo-optical effect. TABLE. 1)
Q = 2325.6759128051194